TCP-connection for real-time simulation

Two possibilities:
1. (green) every MPI-rank has its own TCP-connector (multiple TCP)
2. (red) One MPI-rank collects data and send them (one TCP)

### One TCP:
Aspects:
Idea: Less needed handshakes (one per data transmission), simulator don't has to open several ports (just one) or has to distinct from whom the data came
1. MPI-rank 0 collects data from ranks 1 – n-1
2. Transmits the data
3. Recvs the input data coming from simulator
4. Sends relevant input data to MPI ranks
Implementation in FMI-Master:
1. Using MPI-Writer to collect output data from FMUs
2. Implement a real-time simulation (OpenMP and MPI version) with scheme:

list<solver> L;
frame = 0;
while(run)
simulateFrame(L); //simulate till writeOutput than block
  // MPI/OpenMp-worker
if(checkRecvsTCP(lastFrame + 1 )
++lastFrameM;
inputs = newInputs;
run = newRun;
end if
sendTCP(frame++,getOutputs());
(inFrame,newInputs,newRun) = recvTCP();
if(frame – lastFrame > delay)
wait(inFrame);
speadInputs(inputs);
end while
1. MPI-Writer (getOutputs) only prints normal output times no time events (not needed for real-time simulation)
2. Possible optimization: blocked Worker can clean up DataHistory